## Slide 1: PBCU – HW Modification Proposal
# | Priority | Modification Description | Reason of change | Actual Conf | New Conf | NOTE | Mod life cycle
1 | 1 | +28Vdc Input Filter (U2) replacement | Obsolescence | Schaffner FN409-13 | Custom design |  | CR Can CDAR beapplicable if reverse engineering is performed?
2 | 1 | Replacement of Gate Driver (U34) for 3-phase bridge transistor | Obsolescence | IR2336DS | IR2136STR |  | CDAR
3 | 1 | Add DC Link Overvoltage protection | PR163 | No protection | Regenerative energy dissipation circuit on DC link |  | CR with classic solution To discuss CDAR applicability with Umbra solution
4 | 1 | Modification of triggering threshold for Propeller Speed comparator on HW Security | PR161 |  | Triggering threshold shall be set at 230rpm | Only resistor value modification is requested | CDAR. Functional test to validate the mod
5 | 2 | Main DC/DC converter replacement | New Requirement for max operative temperature | GAIA MGDS-10-J-F/T | Synqor MQBL-28-15S | Synqor is a USA based company Synqor max temp is 125°C Gaia max temp is 105°C | CR. Power input, EMI, Temperature test are at least needed

## Slide 2: PBCU – HW Modification Proposal
# | Priority | Modification Description | Reason of change | Actual Conf | New Conf | NOTE | Mod life cycle
6 | 3 | Replacement of DC/DC converter for CAN bus power supply (+5Vdc) | Reliability and Design maturity improvement and PR165 | Traco TES2N | Linear LTM8046MPY Or equivalent | LTM has BGA Package | CDAR or CR but with limited impact on cert test
7 | 3 | Misc: design improvement based on Raphael findings | Reliability and Design maturity improvement |  |  | Mod List To be shared and agreed | 
8 | 1 | Input Fuse F2 | Reliability and Design maturity improvement | Fuse on PBCU power supply input | No Fuse at PBCU level | No specific requirement to have the Fuse inside the PBCU. | CDAR. No impact on CS-E test