## Slide 1
New Requirement from Airbus (as reported in the Thermal test procedure)
  Ground Survival High Temperature increased to 102 °C
  Operating High Temperature increased to 85 °C
  Short Time Operating High Temperature increased to 102 °C
Original requirement from SP-42N0000-E-EP-06-0066-03
  Ground Survival High Temperature: 85 °C
  Operating High Temperature: 75 °C
  Short Time Operating High Temperature: 85 °C
From HALT Test result:
  UTOL = 95°C.
  At 105°C PBCU was not able to operate.
  no evidence what is the PBCU behaviour in the range 95° to 105°C
EVIDENCES (1/2)

## Slide 2
EVIDENCES (2/2)
The component on the critical thermal path is the DC/DC converter (U1) that it has maximum operative temperature on case equal to 105°C.

## Slide 3
Based on that evidences, regardless the result of thermal test, it is considered risky to standardize PBCU -08 as per new requirement since:
  Thermal test procedure has specific limitation in time to operate PBCU at 102°C, the same limitations are not declared in the requirement.
  At environmental temperature of 102°C there aren’t any margins to operate U1 component. Even if a single PBCU is able to operate according the thermal test procedure, anything could be stated for a wider popolation of PBCU. A certication test with a statistical meaningful number of PBCU is at least needed.
  New thermal evironment requirement will adversly affect the declared MTBF of PBCU
CONCLUSIONS