## Slide 1: TP400 - Pre PDR PBCU hardware Design
X July 2017

## Slide 2: Agenda
TOPICS | Timing (min)
Program context / Objective of the review | 15
List of obsolescence & Maturity Design Obsolescence Management PBCU Reliability (PR / NCR) Design Maturity Improvement Thermal Capabilities Limitations | 30
Answers to Previous Recommandations | 30
Design Evolutions | 30
Verification / Validation / Qualification Plan | 30
Specification Compliance Matrix | 15
Safety Analysis | 15
Development Schedule | 15
Risk Analysis and Mitigation Plan | 20
Conclusion | 20

## Slide 3: PROGRAM CONTEXT
Due to obsolescence, in-services events, to improve the reliability and maturity design, PBCU maturity plan is proposed:
Maturity Plan
Maturity Plan
Thermal
In service Events
Obsolescence
Thermal Capabilities
Limitations
Reliability
Design Maturity
Design
Maturity

## Slide 4: OBJECTIVE OF THE REVIEW
Objective of the review is to define
  PBCU evolutions to be implemanted
  Life modification cycle
  Analysis and test to be performed
  Stategy validation and qualification plan

## Slide 5: List of obsolescence & Maturity Design
N° | Description | Reason of change | comments
1 | +28Vdc Input Filter | Obsolescence | Production impact : end of 2018
2 | Gate Driver for 3-phase bridge transistor | Obsolescence | Introduce a new source in equivalence
3 | Transistor NPN 32V | Obsolescence | Introduce a new source in equivalence
4 | Overvoltage | Reliability | In service events (back EMF failure)
5 | DC/DC converter for CAN bus power | Reliability | Residual humidity on component
6 | Safran Aircraft Engines recommandations | Reliability | 
7 | Fuse | Reliability | In-service events and not requested by EPI
8 | Design error on discrete interface (SVOA & SVOB) | Design maturity improvement | No compliance on Airbus requirement
9 | PBCU HW Security | Design maturity improvement | Not requested by EPI
10 | Thermal Stamp | Design maturity improvement | 
11 | DC/DC converter - Thermal capabilities - Single source | Thermal Capabilities Limitations | Currently, PBCU is standardized up to ISA +22 Airbus requirement is ISA +40

## Slide 6: Obsolescence Management
  Bill Of Material obsolescence status has been provided by Umbra (05/2017)
  3 Obsolescences has been detected :
    Input Filter
    Not equivalent component identified
    Umbra proposes a custom design
    Gate Driver for 3-phase bridge transistor
    An equivalent component has been identified
    Transistor NPN 32V
      An equivalent component has been identified

## Slide 7: PBCU Realiability 1/3
Overvoltage
  Observations
  Treatment PR0163 attached to AR0386
  H-bridge has been damaged by back EMF from PBU. H-bridge does not have dedicated protection hardware against over voltage.
  Proposal solution
  Add dedicated components in order to protect this part

## Slide 8: PBCU Realiability 2/3
DC/DC converter for CAN bus power
  Observations
  Treatment PR0165 : DC/DC converter broken during ATP ESS cycle (-55°C)
  Residual humidity on component or board after long warehouse time
  Proposal solution
  New component identified with package different, not Fit Form Function equivalent so PCB is impacted
Fuse
  Observations
  In service events and no requested by EPI
  The protection is performed before by breaker
  Proposal solution
  Delete the fuse

## Slide 9: PBCU Realiability 3/3
Safran Aircraft Engines recommandations
  Observations
  Observations of PBCU schematics shown design weaknesses
    Instability of Operational Amplifiers in some usages
  Some electronic components are overstressed
    Tantalum capacitors
    Aluminium capacitors
  Minor error in schematics
  Proposal solution
  Safran Aircraft Engines recommandations are described in the presentation attached

## Slide 10: Design Maturity Improvement 1/2
PBCU HW Security
  Observations
  HW security is design in the PBCU but HW Security is not requested by EPI (PR0161)
  Proposal solution
  Modification of triggering threshold for Propeller Speed comparator on HW Security
  No modification with requirement management
  Delete function

## Slide 11: Design Maturity Improvement 2/2
Thermal Stamp
  Observations
  PBCU thermal limit cannot be detected because no thermal sensor is populated inside the PBCU box
  Proposal solution
  Adding of thermal stamps inside the PBCU case to detect over-temperatures

## Slide 12: Thermal Capabilities Limitations
DC/DC converter
  Observations
  Currently, PBCU is standardized up to ISA +22
  Airbus requirement is ISA +40
  Proposal solution : Synqor component
  Perfomance is better than actual component (temperature 125° vs 105°)
  Risks
  Potential export issue (US component)
  2nd solution with many component is not available yet
  New proposal is a single source

## Slide 13: Answers to Previous Recommandations
To be updated by UMBRA

## Slide 14: Design Evolutions 1/2
N° | Description | Reason of change | Solution | MOD Life Cycle | P/N Change | comments
1 | +28Vdc Input Filter | Obsolescence | Custom Design | MOD | No | Production impact : end of 2018
2 | Gate Driver for 3-phase bridge transistor | Obsolescence | Equivalent component | CDAR | No | Introduce a new source in equivalence
3 | Transistor NPN 32V | Obsolescence | Equivalent component | CDAR | No | Introduce a new source in equivalence
4 | Overvoltage | Reliability | Protection of the HW against overvoltage | MOD | No | In service events (back EMF failure)
5 | DC/DC converter for CAN bus power | Reliability | New component | MOD | No | Residual humidity on component
6 | Safran Aircraft Engines recommandations | Reliability | Design Improvement | MOD | No | Improve the reliability
7 | Fuse | Reliability | Fuse is deleted | MOD | No | In-service events and not requested by EPI

## Slide 15: Design Evolutions 2/2
N° | Description | Reason of change | Solutions | MOD Life Cycle | P/N Change | comments
8 | Design error on discrete interface (SVOA & SVOB) | Design maturity improvement |  | MOD | No | No compliance on Airbus requirement
9 | PBCU HW Security | Design maturity improvement | Delete function Modification of triggering threshold No modification of triggering threshold | MOD | No | Not requested by EPI
10 | Thermal Stamp | Design maturity improvement | Thermal Stamp | CDAR | No | 
11 | DC/DC converter - Thermal capabilities - Single source | Thermal Capabilities Limitations | New converter with perfomance is better than the old one Other solution with many components | MOD | Yes | Currently, PBCU is standardized up to ISA +22 Airbus requirement is ISA +40

## Slide 16: Verification / Validation / Qualification Plan 1/2
N° | Description | Reason of change | Reconciliation | Comments
1 | +28Vdc Input Filter | Obsolescence | Power input EMI Vibration Temperature TBC CS-E 80, etc…. | 
2 | Gate Driver for 3-phase bridge transistor | Obsolescence | Analysis | ATP with new component
3 | Transistor NPN 32V | Obsolescence | Analysis | ATP with new component
4 | Overvoltage | Reliability | Vibration Temperature TBC | 
5 | DC/DC converter for CAN bus power | Reliability | Vibration Temperature TBC | 
6 | Safran Aircraft Engines recommandations | Reliability | Analysis | ATP with new component
7 | Fuse | Reliability | Analysis | 
To be updated by UMBRA

## Slide 17: Verification / Validation / Qualification Plan 2/2
N° | Description | Reason of change | Reconciliation | comments
8 | Design error on discrete interface (SVOA & SVOB) | Design maturity improvement |  | 
9 | PBCU HW Security | Design maturity improvement | Depending solution | 
10 | Thermal Stamp | Design maturity improvement | Analysis | 
11 | DC/DC converter - Thermal capabilities - Single source | Thermal Capabilities Limitations | Power input EMI Vibration Temperature TBC | 
To be updated by UMBRA

## Slide 18: Safety Analysis
To be updated by UMBRA

## Slide 19: Development Schedule
To be updated by UMBRA

## Slide 20: Risk Analysis and Mitigation Plan
# | Item | Description | Actions | Responsible | Probability X Gravity
1 |  |  |  |  | 
2 |  |  |  |  | 
3 |  |  |  |  | 
To be updated by
Safran Aircraft Engines & UMBRA

## Slide 21: Conclusion
To be updated by
Safran Aircraft Engines & UMBRA